## Slide 1: 0.39’’ AR HUD PGU Optical Design
HUD PGU Reference Design
August 2025

## Slide 2
IMPORTANT NOTICE FOR TI REFERENCE DESIGNS
Texas Instruments Incorporated (‘TI”) reference designs are solely intended to assist designers (“Designer(s)”) who are developing systems that incorporate TI products. TI has not conducted any testing other than that specifically described in the published documentation for a particular reference design.
TI’s provision of reference designs and any other technical, applications or design advice, quality characterization, reliability data or other information or services does not expand or otherwise alter TI’s applicable published warranties or warranty disclaimers for TI products, and no additional obligations or liabilities arise from TI providing such reference designs or other items.
TI reserves the right to make corrections, enhancements, improvements and other changes to its reference designs and other items.
Designer understands and agrees that Designer remains responsible for using its independent analysis, evaluation and judgment in designing Designer’s systems and products, and has full and exclusive responsibility to assure the safety of its products and compliance of its products (and of all TI products used in or for such Designer’s products) with all applicable regulations, laws and other applicable
requirements. Designer represents that, with respect to its applications, it has all the necessary expertise to create and implement safeguards that (1) anticipate dangerous consequences of failures, (2) monitor failures and their consequences, and (3) lessen the likelihood of failures that might cause harm and take appropriate actions. Designer agrees that prior to using or distributing any systems that include TI products, Designer will thoroughly test such systems and the functionality of such TI products as used in such systems.
Designer may not use any TI products in life-critical medical equipment unless authorized officers of the parties have executed a special contract specifically governing such use. Life-critical medical equipment is medical equipment where failure of such equipment would cause serious bodily injury or death (e.g., life support, pacemakers, defibrillators, heart pumps, neurostimulators, and implantables). Such equipment includes, without limitation, all medical devices identified by the U.S. Food and Drug Administration as Class III devices and equivalent classifications outside the U.S.
Designers are authorized to use, copy and modify any individual TI reference design only in connection with the development of end products that include the TI product(s) identified in that reference design. HOWEVER, NO OTHER LICENSE, EXPRESS OR IMPLIED, BY ESTOPPEL OR OTHERWISE TO ANY OTHER TI INTELLECTUAL PROPERTY RIGHT, AND NO LICENSE TO ANY TECHNOLOGY OR
INTELLECTUAL PROPERTY RIGHT OF TI OR ANY THIRD PARTY IS GRANTED HEREIN, including but not limited to any patent right, copyright, mask work right, or other intellectual property right relating to any combination, machine, or process in which TI products or services are used. Information published by TI regarding third-party products or services does not constitute a license to use such products
or services, or a warranty or endorsement thereof. Use of the reference design or other items described above may require a license from a third party under the patents or other intellectual property of the third party, or a license from TI under the patents or other intellectual property of TI.
TI REFERENCE DESIGNS AND OTHER ITEMS DESCRIBED ABOVE ARE PROVIDED “AS IS” AND WITH ALL FAULTS. TI DISCLAIMS ALL OTHER WARRANTIES OR REPRESENTATIONS, EXPRESS OR IMPLIED, REGARDING THE REFERENCE DESIGNS OR USE OF THE REFERENCE DESIGNS, INCLUDING BUT NOT LIMITED TO ACCURACY OR COMPLETENESS, TITLE, ANY EPIDEMIC FAILURE WARRANTY AND ANY IMPLIED WARRANTIES OF MERCHANTABILITY, FITNESS FOR A PARTICULAR PURPOSE, AND NONINFRINGEMENT OF ANY THIRD PARTY INTELLECTUAL PROPERTY RIGHTS. TI SHALL NOT BE LIABLE FOR AND SHALL NOT DEFEND OR INDEMNIFY DESIGNERS AGAINST ANY CLAIM, INCLUDING BUT NOT LIMITED TO ANY INFRINGEMENT CLAIM THAT RELATES TO OR IS BASED ON ANY COMBINATION OF PRODUCTS AS DESCRIBED IN A TI REFERENCE DESIGN OR OTHERWISE. IN NO EVENT SHALL TI BE LIABLE FOR ANY ACTUAL, DIRECT, SPECIAL, COLLATERAL, INDIRECT, PUNITIVE, INCIDENTAL, CONSEQUENTIAL OR EXEMPLARY DAMAGES IN CONNECTION WITH OR ARISING OUT OF THE REFERENCE DESIGNS OR USE OF THE REFERENCE DESIGNS, AND REGARDLESS OF WHETHER TI HAS BEEN ADVISED OF THE POSSIBILITY OF SUCH DAMAGES.
TI’s standard terms of sale for semiconductor products (http://www.ti.com/sc/docs/stdterms.htm) apply to the sale of packaged integrated circuit products. Additional terms may apply to the use or sale of other types of TI products and services. Designer will fully indemnify TI and its representatives against any damages, costs, losses, and/or liabilities arising out of Designer’s noncompliance with the terms and provisions of this Notice.
Mailing Address: Texas Instruments, Post Office Box 655303, Dallas,

## Slide 3: Optical Design Layout
.39’’ Auto DMD :
Active array dimension: 8.708mm x 4.918mm
Side illumination
4.5um diamond pixel
Mirror tilting angle: +/-14.5 deg
Design spec overview:
F/2.4 Both illumination and projection
Telecentric illumination and projection
Source LED: Osram Q8WP
Dimension: 86mm x 59mm x 28mm (20mm if trim relay lens)
Prism material: N-SF8
2 options for illumination design
  Standard design
  Scheimpflug method for sun glare reduction (20 deg screen tilt) with modified illumination to compensate added DMD tilt (2.53deg)
Relay lens may be trimmed for smaller dimension

## Slide 4: F/# Selection
Select F/2.4 for contrast >2000:1
Efficiency Smaller projection lens size
DMD Efficiency ~ 55% (used for lumen budget)
Expected contrast and efficiency for well stray light managed system
Photopic weighted measurements

## Slide 5: LED Options – Selected Osram Q8
F/2
F/2.3
F/2.4
Best Matched LEDs
@F/2: P1 , Q7, Q8, PT-26
@F/2.3: Q8 or PT-26
@F/2.4: Q8 or PT-26
Not Auto-qualified
Selected for design

## Slide 6: Lumen Budget - F/2.4
Assumptions for lumen budget:
D65 colorpoint
Diffraction efficiency: 0.55@F/2.4
100% duty cycle
LED: Avg Bin
Sequence efficiency: 0.97
Temperature: 25C
Assumes 3C/W heatsink thermal resistance
Design with no Scheimpflug
Design with Scheimpflug: Geometric efficiency: 58.1%
Total lumens @ 262lm
100% duty cycle
Important note: Actual projected lumens will be lower than simple prediction due to:
Additional auto sequence loss
Duty cycle (for example 90/10 or 80/20)
LED temperature and thermal design

## Slide 7: Geometric Efficiency @ DMD Plane
Active array
B
G
R
RGB
Overfill
17.1%
16.5%
16.5%
18.3%
61.4%
65.1%
68.5%
65%
Note: Overfill efficiency number includes flyeye crosstalk within the image size

## Slide 8: Geometric Efficiency @ DMD Far-field & Image
B
G
R
RGB
DMD Far-field
Image Plane
62.5%
66.3%
61.7%
59.4%
58.3%
60.5%
64.6%
61.1%

## Slide 9: Illumination aperture
Add physical metal aperture at exit of FEA
Physical aperture defines the f/# of illumination
Setting the f/# of illumination with an aperture minimizes the risk of stray light artifacts in the projected image
Illumination stop aperture goes here

## Slide 10: Telecentric Projection Lens Design & MTF Plot
Projection lens:
  7 elements (all glass, spherical, air spaced singlets)
  0% offset
  Pupil distance from screen: 174.6mm
  Image size: 73 x 41.3mm
  Image location (from last lens vertex): 150mm
  Lateral color: <0.56 pixel
  MTF@110lp/mm >49% across whole field
  Distortion: <0.47%

## Slide 11: Lateral Color & Distortion
~2.5um / 4.5um = 0.56pixel Lateral color B-R
Max distortion: -0.47%

## Slide 12: Scheimpflug for Sun Glare Reduction
HUD glare is caused by sunlight reflections from diffuser screen returning to the eyebox. When the sun in within the FOV (as seen upwards through windshield) the sunlight fills the primary mirror aperture and reflects off of the diffuser screen. Specular reflections from the screen surface can return through the optics, enter the eyebox and be seen by the driver as a brilliant glare. The primary mitigation method for screen glare is a tilt of the diffuser screen.
Using Scheimpflug method(adding a small tilt angle to the DMD) can be useful in DLP PGU design to create a sharp image focus when using a tilted diffuser for minimizing solar glare.
External Light
Specular reflection
With screen tilt: specular reflection is redirected away from eyebox to be absorbed elsewhere in the HUD system
Light cone collected by HUD optics (visible in eyebox)
Diffuse reflectance scattering profile
Diffuser screen
External Light
Specular reflection
Visible to driver
  Tilting screen will help minimize backscatter glow.

## Slide 13: Scheimpflug for Sun Glare Reduction
DMD tilting angle: 2.532 deg
Center of screen chief ray angle to screen normal: 20 deg
Diffuser screen tilt of 20 deg to optical axis of projection lens

## Slide 14: Distortion and MTF Plot with Scheimpflug
Max: 5.04%

## Slide 15: Geometric efficiency with Scheimpflug at Image Plane No Modification at Illumination
50.7%
Exaggerated tilting angle at DMD
(actual angle at DMD is 2.53deg)
With added tilt angle to DMD for Shiempflug, the light onto the DMD will no longer at 29deg but a compound X and Y incidence angle. Light entering the projection lens is no longer centered on the pupil, resulting in efficiency loss.
We have modified the illumination angle on the DMD to compensate for the added tilt to DMD due to the Scheimpflug condition.
Exaggerated tilting angle at DMD
(actual angle at DMD is 2.53deg)
Light goes into the projection lens is no longer centered at the pupil

## Slide 16: Geometric efficiency with Scheimpflug Modified Illumination to compensate added 2.53deg DMD tilt and maintain low angle(~1deg) to projection lens
RGB 58.2%
G
B
R
To compensate the added tilt at DMD, the illumination is constrained to be 29deg entering the DMD, and light exiting the prism surface is constraint to be around 1 deg.
This modification will add in a twist to the design, but the light entering the projection lens is centered back to the projection lens pupil to achieve higher efficiency.

## Slide 17: Summary
Design Spec:
F/2.4 both illumination and Projection for >2000:1 FOFO contrast
Light source: Osram Q8WP LEDs
Optic layout dimensions ~ 86mm x 59mm x 28mm (20mm if trim relay lens)
For HUD design use reference design with Scheimpflug
  Design with Scheimpflug with tilted diffuser screen for sun glare reduction [STRONGLY RECOMMENDED]
    20 deg screen tilt and modified illumination to compensate added DMD tilt of ~ 2.53 degrees
    62.1% geometric efficiency, lumen estimation at 262 lm (before duty cycle, thermal considerations and sequence loss)
For Waveguide HUD or interior displays (designs that do not require sunlight glare mitigation) use Reference design without Scheimpflug
  Regular design (no Scheimpflug image tilt)
    65.1% geometric efficiency, lumen estimation at 275 lm (before duty cycle, thermal considerations and sequence loss)
Two available optical reference designs